## Slide 1
NXP S32K118 FIRMWARE更新架構
00000000H
0000A000H
NXP S32K PFlash
bootloader
(40K Bytes)
application program
(216K Bytes)
CAN programmer
e.g, EZCAN
UpdateMcuApp.exe
CAN
interface
MCU
以CAN bus當作更新firmware的介面
bootloader與application為各自獨立的兩個專案
在application端亦須預留CAN bus,使其能接收來自PC端觸發更新的command
(跳回bootloader更新)

## Slide 2
ROM
SFR
(pheripheral)
00000000H
PFlash
FlashNVM
ARM Cortex-M0
Vector Table
+
40000000H
1C000000H
RAM
NXP S32K Interrupt
Vector Table
0H
10H
C0H
Reserved
IFR
3C0H
400H
bootloader
/User program
NXP S32K118 的 MEMORY MAP
其中:
address 0H :儲存一個位址¸此位址之後會提供給core register 的 SP 指標暫存器
address 4H:儲存一個位址,此位址會提供給 core register 的 PC 指標暫存器
offset +0h +4h

## Slide 3
LINKER SCRIPT FILE
bootloader linker file settings:
application linker file settings:

## Slide 4
RELOCATE THE ADDRESS BEFORE JUMPING TO APP(1)
bootloader 程式以及app程式為各自獨立的專案,所以在編譯之後會產生各自所屬的中段向量表,假設bootloader在完成app更新之後且確認app為有效的,當欲從bootloader jump到app執行時,我們須對MCU的兩個 core registers 外加一個vector offset register做設定
1. VTOR (Vector Table Register):
Application code 所屬vector table的起始位址, 在編譯app的時候,我們透過
linker scrupt file 將向量表設置在app image的最前端的位址, 而vector table裡
面包含兩個訊息, 其一為ARM Cortex -M0基本的中斷向量表 (offset 0H~FH),
其二為NXP S32K 的中斷向量表 (10H~)
// Update the vector table to the reset vector of the application.
S32_SCB->VTOR = (uint32_t)MEM_APP_START;
2. PC (Program Counter) :
Application code 程式進入點的位址 (也就是程式中Starup code裡面的Reset Handler
所在的位址), 而這個資訊會儲存在application image 的offset 4h
// Point to the start reset vector for the application.
p_jump_to_app = ((uint32_t)MEM_APP_START+4);
3. SP(Stack Pointer):
application code 使用stack的起始位址, 這個位址資訊可以從Vector table的offset
0H 裡面找到
//Set stack for the application
MSR_MSP(*(volatile uint32_t*)MEM_APP_START);

## Slide 5
VTOR
0xE000ED08
A000H
RELOCATE THE ADDRESS BEFORE JUMPING TO APP(2)
bootloader vector table
application vector table
bootloader
Reset Handler of
application
A4C4H
APP IMAGE EXAMPLE:
結果:
VTOR = 0xA000
SP = 0x20005800 (stack 在RAM的位址)
PC = 0xA4C5 (Thumb 指令集), 實際上會從
0xA4C4執行
0000H

## Slide 6
FIRMWARE UPDATE FLOW
START
board init
enable CAN
receive
g_can_rx_complete = false
firmware update loop and waiting command from PC
Y
timeout?
Y
N
N
A
A
Jump to app
application = valid?
software reset
Y
N

## Slide 7
Win App + NXP : Flow
Command | Send | Step | Action
Update | Win App | 1 | 1. Tell Application or Bootloader to start the process 2. Win App delay some time
 | NXP | 2 | Response
Erase | Win App | 3 | Tell Bootloader to erase flash
 | NXP | 4 | Response
Addr | Win App | 5 | Tell Bootloader address
 | NXP | 6 | Response
Data | Win App | 7 | 1. Send data 2. Will repeat step 5,6,7,8 until finish all data
 | NXP | 8 | Response
End | Win App | 9 | Finish
 | NXP | 10 | 1. Response 2. Restart MCU

## Slide 8
Win App + NXP : Command context
Command | Send | ID | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
Update | Win App | 0x100 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00
 | NXP | 0x101 | Pass : 00 Fail : Other | 00 00 | 00 00 | 00 00 | 00 00 | 00 00 | 00 00 | 00 00
Erase | Win App | 0x200 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00
 | NXP | 0x201 | Pass : 00 Fail : Other | 00 00 | 00 00 | 00 00 | 00 00 | 00 00 | 00 00 | 00 00
Addr | Win App | 0x300 | 00 | 00 | 00 | 00 | A3 | A2 | A1 | A0
 | NXP | 0x301 | Pass : 00 Fail : Other | 00 00 | 00 00 | 00 00 | 00 00 | 00 00 | 00 00 | 00 00
Data | Win App | 0x400 | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
 | NXP | 0x401 | Pass : D0 Fail : Error code | D1 00 | D2 00 | D3 00 | D4 00 | D5 00 | D6 00 | D7 00
End | Win App | 0x500 | 00 | 00 | 00 | 00 | 00 | 00 | 00 | 00
 | NXP | 0x501 | Pass : 00 Fail : Other | 00 00 | 00 00 | 00 00 | 00 00 | 00 00 | 00 00 | 00 00